## Slide 1: uart6551
uart6551
Gnd
dat_i[31:8]
cyc_i
stb_i
Active high chip select
sel_i[3:1]
adr_i[2]
adr_i[3]
a0
a1
rst_i
Active high reset
cs_i
irq_o
Open collector buffer
E.g. 74ls06
d0 to d7
dat_i[7:0]
Notes:
The irq output is active high and not tri-state or open collector
so will need an inverting buffer.
The reset input is active high and may need an inverting buffer from
an active low reset.
Chips select / valid cycle signals are also active high.
ack_o needs to be gated into the CPU’s RDY signal. Output data is valid only when ack_o is high. Since ack_o is high only if the circuit is selected it may also need to be gated with the circuit select signal to keep RDY high when uart6551 is not selected.
dat_o[31:8]
dat_o[7:0]
d0 to d7
Tri-state buffer, connected to cs and r/w
E.g. 74ls244 / 245
ack_o
nc
clk_i
ph02
Nand
74ls00
Active high chip select
ack_o
inverter
rdy